Table 1 The defined Criteria and Decision Rules for Route Selection

| Alternative | Criteria | Decision rules |
| --- | --- | --- |
| Economy | Slope | Maximizing route length in flat and mild slopes to reduce cut and fill costs. |
|  | Land Use | Minimizing route length in agriculture, and urban areas to avoid land acquisition. |
|  | Faults | Faults are considered a constraint in routing a highway and should be avoided to reduce cost. |
|  | Rock Type | Minimizing route length in Rock areas to avoid high amounts of cut and fill costs. |
|  | Hydrology | Minimizing route length intersecting stream networks to avoid flood protection constructions. |
|  | Sand Dunes | Minimizing route length intersecting sand dunes to avoid the risk of dunes encroachment on the highway. |
| Environmental | Agriculture Distance | Maximizing route distance from agricultural areas to avoid loss of rural lands. |
|  | Stream Distance | Maximizing route distance from water stream networks to preserve the water resource. |
|  | Sand Dunes | Far from sand dunes areas to avoid problems that may be caused by dunes encroachment on driving and road safety. |
|  | Archaeology sites | Archaeology sites are cultural and historical values. Such sites should not be crossed by the highway. |

Table 2 Data sources and derived item

| Data | Date | Source | Derived Item |
| --- | --- | --- | --- |
| Shuttle Radar Topography Mission (SRTM) Data | March 2018 | SRTM GDEM http://www.gdem.SRTM.ersdac.or.jp | Extraction of Digital Elevation Model (DEM), slope, and stream network. |
| Landsat 8 (OLI) Images | June 2018 | Landsat 8(OLI) | Extraction of the Land cover map, sand dunes |

Table 3 Standardized Economy Values

| Standardized Economy Values | Cost value |
| --- | --- |
| Economy Theme | Slope (%) [3] | 0–3 | 1 |
|  |  | 3-5 | 2 |
|  |  | 5-8 | 3 |
|  |  | 8-10 | 4 |
|  |  | 10-15 | 5 |
|  |  | 15-18 | 6 |
|  |  | 18-20 | 7 |
|  |  | 20-25 | 8 |
|  |  | >25 | 9 |
|  | Land use [1] | Water, Sand dunes, Urban, Mountainous rocks | 9 |
|  |  | Agriculture | 6 |
|  |  | Natural Vegetation | 4 |
|  |  | Bare Rock with shallow sand | 1 |
|  | Faults (Effat and Hassan 2013) | Fault | 9 |
|  |  | No faults | 1 |
|  | Hydrology | Stream | 9 |
|  |  | No streams | 1 |
|  | Sand dunes | Sand dunes | 9 |
|  |  | No sand dunes | 1 |
|  | Rock type [15] | Basalt, Quartz, Lake | 9 |
|  |  | Gypsum, Lime Stone | 5 |
|  |  | Pebbles | 3 |
|  |  | Clay, Shale, Marl, Sand Stone | 2 |
|  |  | Agriculture | 4 |

Table 4 Standardized Environmental Values

| Standardized Environmental Values | Cost Value |
| --- | --- |
| Environmental | Proximity to Agriculture (km) [14] | 0-0.1 | 9 |
|  |  | 0.1-0.2 | 6 |
|  |  | 0.2-0.3 | 3 |
|  |  | >0.3 | 1 |
|  | Proximity to Streams (km) [14] | 0-1 | 9 |
|  |  | 1-2 | 6 |
|  |  | 2-3 | 3 |
|  |  | >3 | 1 |
|  | Protectorate [1] | Present | 9 |
|  |  | Under Research | 5 |
|  |  | No | 1 |
|  | Proximity to Sand Dunes (km) | 0-0.1 | 9 |
|  |  | 0.1-0.2 | 6 |
|  |  | 0.2-0.3 | 3 |
|  |  | >0.3 | 1 |

Table 5 AHP Weighting full example: Economy Weighting

| Pairwise comparisons |
| --- |
| Factors | Slope | Land use | Faults | Rock Type | Stream | Sand dunes |
| Slope | 1 | 9/7 | 9/3 | 9/5 | 9/4 | 9/3 |
| Land use | 7/9 | 1 | 7/3 | 7/5 | 7/4 | 7/3 |
| Faults | 3/9 | 3/7 | 1 | 3/5 | 3/4 | 3/3 |
| Rock Type | 5/9 | 5/7 | 5/3 | 1 | 5/4 | 5/3 |
| Stream | 4/9 | 4/7 | 4/3 | 4/5 | 1 | 4/3 |
| Sand dunes | 3/9 | 3/7 | 3/3 | 3/5 | 3/4 | 1 |
| SUM | 3.68 | 4.43 | 10.33 | 6.20 | 7.75 | 10.33 |

Table 6 Normalized pairwise AHP comparison matrix and relative weights

| Factors | Slope | Land use | Faults | Rock Type | Stream | Dunes | Weighting |
| --- | --- | --- | --- | --- | --- | --- | --- |
| Slope | 0.27 | 0.29 | 0.29 | 0.29 | 0.29 | 0.29 | 28.7 |
| Land use | 0.21 | 0.23 | 0.23 | 0.23 | 0.23 | 0.23 | 22.3 |
| Faults | 0.09 | 0.10 | 0.10 | 0.10 | 0.10 | 0.10 | 9.6 |
| Rock Type | 0.15 | 0.16 | 0.16 | 0.16 | 0.16 | 0.16 | 16 |
| Stream | 0.12 | 0.13 | 0.13 | 0.13 | 0.13 | 0.13 | 12.8 |
| Dunes | 0.16 | 0.10 | 0.10 | 0.10 | 0.10 | 0.10 | 10.7 |
| SUM |  | 100% |

Table 7 AHP Weighting for environmental vision

| Pairwise comparisons |
| --- |
| Factors | Proximity to | Protectorates |
|  | Stream | Dunes | Agriculture |  |
| Proximity to Stream | 1 | 5/3 | 5/5 | 5/7 |
| Proximity to Sand dunes | 3/5 | 1 | 3/5 | 3/7 |
| Proximity to Agriculture | 5/5 | 5/3 | 1 | 5/7 |
| Protectorates | 7/5 | 7/3 | 7/5 | 1 |
| SUM | 4 | 6.67 | 4 | 2.86 |

Table 8 Normalized pairwise AHP comparison matrix and relative weights

| Factors | Proximity to | Protectorates | Weighting |
| --- | --- | --- | --- |
|  | Stream | Dunes | Agriculture |  |  |
| Proximity to Stream | 0.25 | 0.25 | 0.25 | 0.25 | 25.0% |
| Proximity to dunes | 0.15 | 0.15 | 0.15 | 0.15 | 15.0% |
| Proximity to Agriculture | 0.25 | 0.25 | 0.25 | 0.25 | 25.0% |
| Protectorates | 0.35 | 0.35 | 0.35 | 0.35 | 35.0% |
| SUM |  | 100% |

| Research Case | Alternatives |
| --- | --- |
|  | Economy | Environmental |
| I- Economy Vision | 0.7 | 0.3 |
| II- Environmental Vision | 0.3 | 0.7 |
| III- Equal Vision | 0.5 | 0.5 |
| IV – Economy Only Vision | 1.0 | 0 |

Table 9 Assigned Weights for Multiple Research Cases

Table 10 Different Criterion Based on Multiple Research Cases

| Attribute | MCDA-Case Research |
| --- | --- |
|  | Economy | Environmental | Equal | Economy Only |
| Slope Crossing (>15%) (m) | 4,448 | 16,018 | 6,887 | 2,094 |
| Basement Rock Crossing (m) | 15,950 | 25,792 | 6,556 | 11,019 |
| Length of road(m) crossing Stream buffer zone 300m | 1911 | 1004 | 907 | 3,739 |
| Length of road(m) crossing fault buffer zone 500m | 0 | 1,267 | 675 | 440 |
| Proximity to stream | 16417 | 10,111 | 9,349 | 124,664 |
| Protectorates Crossing (m) | 29,799 | 3,059 | 3,348 | 30,738 |
| Route Length(m) | 225,017 | 209,322 | 216,078 | 226,285 |

Table 11 Pairwise comparison matrix used for calculation of weights for the evaluation criteria

| Criteria | Slope Crossing | Rock Crossing | Stream Crossing | Faults | Prox. to Stream | Prot. Crossing | Route Length | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Slope Crossing>15% | 1 | 1.8 | 2.25 | 3 | 2.25 | 1.5 | 2.25 | 0.25 |
| Rock Crossing | 0.56 | 1 | 1.25 | 1.67 | 1.25 | 0.83 | 1.25 | 0.14 |
| Stream Crossing | 0.44 | 0.8 | 1 | 1.33 | 1 | 0.67 | 1 | 0.11 |
| Faults | 0.33 | 0.6 | 0.75 | 1 | 0.75 | 0.5 | 0.75 | 0.08 |
| Proximity to Stream | 0.44 | 0.8 | 1 | 1.33 | 1 | 0.67 | 1 | 0.11 |
| Protectorates Crossing | 0.8 | 1.2 | 1.5 | 2 | 1.5 | 1 | 1.5 | 0.17 |
| Route Length | 1 | 0.8 | 1 | 1.33 | 1 | 0.67 | 1 | 0.13 |

Table 12 Comparison among Road Specifications regarding Different

| Attribute | Comparison |
| --- | --- |
|  | Equal | Existing |
| Rock Crossing(m) | 6,556 | 17,816 |
| Stream Crossing(m) | 907 | 43,785 |
| Faults Crossing(m) | 675 | 898 |
| Route Length(m) | 216,078 | 224,000 |

Table 13 Different Criterion Based on Multiple Research Cases

| Attribute | MCDA-Case Research |
| --- | --- |
|  | Economy | Environmental | Equal | Economy Only |
| Slope Crossing >15%) (m) | 485 | 641 | 461 | 402 |
| Rock Crossing(m) | 6,705 | 7,314 | 7,132 | 6,700 |
| Stream Crossing(m) | 784 | 784 | 784 | 984 |
| Faults Crossing(m) | 0 | 503 | 0 | 0 |
| Proximity to stream | 11,540 | 11,950 | 11,561 | 9,129 |
| Proximity to Agriculture land(m) | 12,308 | 4,171 | 5,478 | 67,757 |
| Sand dunes Crossing (m) | 7,199 | 8,156 | 7,530 | 7,335 |
| Route Length(m) | 185,246 | 183,882 | 184,597 | 180,206 |

Table 14 Pairwise comparison matrix used for calculation of weights for the evaluation criteria

| Factors | Slope | Rock Crossing | Stream Crossing | Faults Crossing | Prox. to Stream | Prox. to agri. land | Sand dunes Crossing | Route Length | Weight |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| Slope | 1.00 | 1.80 | 2.25 | 3.00 | 2.25 | 1.29 | 3.00 | 2.25 | 0.22 |
| Rock Crossing | 0.56 | 1.00 | 1.25 | 1.67 | 1.25 | 0.71 | 1.67 | 1.25 | 0.12 |
| Stream Crossing | 0.44 | 0.80 | 1.00 | 1.33 | 1.00 | 0.57 | 1.33 | 1.00 | 0.10 |
| Faults Crossing | 0.33 | 0.60 | 0.75 | 1.00 | 0.75 | 0.57 | 1.00 | 0.75 | 0.08 |
| Prox. to Streams | 0.44 | 0.80 | 1.00 | 1.33 | 1.00 | 0.57 | 1.33 | 1.00 | 0.10 |
| Proximity to agri. land | 0.80 | 1.40 | 1.75 | 1.75 | 1.75 | 1.00 | 2.33 | 1.75 | 0.17 |
| Sand dunes Crossing | 1.00 | 0.60 | 0.75 | 1.00 | 0.75 | 0.43 | 1.00 | 0.75 | 0.09 |
| Route Length | 1.33 | 0.80 | 1.00 | 1.33 | 1.00 | 0.57 | 1.33 | 1.00 | 0.12 |

Table15 Comparison among Road Specifications regarding Different

| Attribute | Comparison |
| --- | --- |
|  | Equal | Existing |
| Slope Crossing (>15%) (m) | 461 | 318 |
| Rock Crossing(m) | 7,132 | 12,553 |
| Stream Crossing(m) | 784 | 1,473 |
| Faults Crossing(m) | 0 | 1,621 |
| Proximity to stream | 11,561 | 16,118 |
| Proximity to Agriculture land(m) | 5,478 | 44,948 |
| Sand dunes Crossing (m) | 7,530 | 13,479 |
| Route Length(m) | 184,597 | 197,988 |